## Slide 1
Basic Usage Training Session
Version 2.0
Friday, July 19th, 2013
Khushboo Bindlish
Secure Boot Tools

## Slide 2
Tools
ISU
FITC
Xfstk-stitcher

## Slide 3
Revision History
July 19’2013 – Added PDR Signing to slides 15 and 16.

## Slide 4
What You Need to Know
Basic Structure of a Manifest
Hash Payloads
Manifest Signature
Public Key Exponent
Public Key Modulus
RSA
Sign
Hash
Derived
Public
Key
Private
Key
1KB

## Slide 5
What You Need to Know (cont)
The root of trust for all the manifests is the Fuse File
SB Enable
Key Manifest ID
OEM Public Key Hash
Fuse File
Key
Manifest
Secure Boot/
PDR Manifest
Secure Boot Manifest Key
Hash
Signed
Signed
Key Manifest ID = 0
Signed
Key Manifest ID <> 0
OS Manifest Key
Hash
Key Manifest ID <> 0
Hash
Key Manifest ID = 0
OS
Manifest
Signed
Signing Manifest
Embedding Hash
OEM Key
Hash

## Slide 6
What You Need to Determine Before Starting
Tag Name for Manifest (typically part of the IAFW file name, i.e. Bstep36S)
Key Manifest ID (0 = no Key Manifest, 1 to 63 = Key Manifest)
Secure Version Number (SVN, non-zero value, typically starts at 1 but may be other values, especially during ARB testing)
Is an OS Manifest and/or PDR Manifest going to be included (these are optional with the tool but for BayTrail there will always be an OS Manifest and a PDR Manifest)

## Slide 7
What You Need to Get Before Starting
Fuse Configuration Template File
OEM Public Key (i.e. OEM_pub.pub)
OEM Private Key (i.e. OEM_priv.pem)
Secure Boot Manifest Public Key (i.e. SB_pub.pub)*
Secure Boot Manifest Private Key (i.e. SB_priv.pem)*
OS Image File (i.e. no_osip_boot.bin) †
OS Manifest Public Key (i.e. OS_pub.pub) †
OS Manifest Private Key (i.e. OS_priv.pem) †
Boot ROM File (IBB1 image or IAFW image)
PDR Data File (64k image) ‡
OEM Data File§
* -Not needed if Key Manifest ID is set to 0
† -Not needed if OS Manifest is not included (but OS Manifest is always included on BayTrail)
‡ -Not needed if PDR Manifest is not included (but PDR Manifest is always included on BayTrail)
§ -Not needed if Boot ROM file is an IAFW image

## Slide 8
ISU – Intel Signing Utility
ISU is used to sign firmware or Operating System (OS) binaries.
Usage:
./isu [options]
-i, Name of input file to use
-o, Name of output file to use
-l, PEM formatted key to use for signing
-t, Image type to sign (os_binary-6, iafw-cfg-7, hash-key-10)
-v, SVN ID
-p, Platform type to use for signing(optional)
(0-MFLD, 1-CLVP, 2-BYT: default 1)
- y, In case of IAFW Signing, whether to create Key Manifest or not ( 0 – zero KM, 1 – non-zero KM)

## Slide 9
ISU for Baytrail
Create OS manifest given a boot.bin
Create Hash of a key
Create Secure Boot Manifest and Key Manifest for IAFW.

## Slide 10
Preparing Fuse Configuration File
Run ISU tool to generate a hash of the OEM public key, thus:
./isu -t 10 -p 2 -i OEM_pub.pub -o OEM_KEY_HASH
Copy and paste the contents of OEM_public_key_hash.txt into the value field of the FUSE_FILE_OEM_KEY_HASH_1 entry in the fuses.txt file.
Set the value field of the FUSE_FILE_KEY_MANIFEST_ID entry to the ID value that you have determined for this build (entry must be two digits, leading 0’s required for values 0 to 9).
Set the value field of the FUSE_FILE_SECURE_BOOT_EN to 01.

## Slide 11
Fuses.txt File Example
FUSE_FILE_SECURE_BOOT_EN:01:FALSE
FUSE_FILE_GLOBAL_VALID:00:FALSE
FUSE_FILE_TPM_DISABLE:00:FALSE
FUSE_FILE_OEM_KEY_HASH_1:B59D5E9B5148BE6C3CFCC62D9A14F64EC916FEC341367895E5DAB730F7804C36:FALSE
FUSE_FILE_ALT_BIOS_LIMIT:0000:FALSE
FUSE_FILE_KEY_MANIFEST_ID:01:FALSE

## Slide 12
Flow for SB Manifest
Manifest
Create
Manifest
Complete
Manifest
Signature
Manifest
Public
Key
Manifest.bin
Fuse
Configuration
File
Manifest
Private
Key
Other
Data Files
& Parameters
Manifest
Workspace
Secure Facility
Manifest
Hash
Manifest
Signature
ISU

## Slide 13
To get final IFWI
IFWI
Manifest.bin
Manifest
5k
8MB
FITC
Fuse
Configuration
File
Final Signed IFWI
IBB
127k

## Slide 14
Flow for OS Signing
Manifest
Create
Manifest
Complete
Manifest
Signature
OS Public Key
Manifest.bin
Boot.bin (no OSIP header)
OS
Private
Key
Manifest
Workspace
Secure Facility
Manifest
Hash
Manifest
Signature
ISU
Boot.bin (no OSIP header)
Manifest
1K
Xfstk-stitcher
Boot.bin
Notes: 1. Flash an unsigned IFWI
2. Flash a signed OS
3. Flash the signed IFWI
<number>

## Slide 15
Signing IAFW using ISU (and PDR Signing)
Generate the Secure Boot Manifest (with Key Manifest ID = 0)
./isu -t 7 -p 2 -i iafw_cfg_byt_KM_zero.txt -o SBmanifest -y 0
Generate the Secure Boot Manifest (with Key Manifest ID = 1 to 63)
./isu -t 7 -p 2 -i iafw_cfg_byt_KM_non_zero.txt -o SBmanifest -y 1
This command is also used for PDR Signing. See Next slide for configuration file. Based on the configuration file, this command will cause ISU to sign either IAFW or PDR Region or both.

## Slide 16
Iafw_cfg_byt.txt File Example

## Slide 17
Creating IFWI
Stitch the SB Manifest into the IFWI
dd if=Bstep36S_SB_manifest.bin of=VLV_FLASH_IMAGE_BIOS_MCG.bin seek=$((1024*8-132)) bs=1K count=5 conv=notrunc
Configure fuses into the IFWI
FITC lets the user change a flash image’s configuration. It can be used to configure mirrored fuses into the image.
  Launch FITC
  File->Open-> Choose original IFWI
  Navigate to Flash Image-> TXE Region-> TXE -> Intel® FPF Mirroring File
  Double click and choose the mirror file.
  Build-> Build Image or F5 to get the new IFWI.
Flash the IFWI.

## Slide 18
Using FITC for configuring fuses

## Slide 19
Signing OS for BYT
./isu -i no_osip_boot.bin -o manifest_name -l OS_priv.pem -v 1 -t 6 -p 2
In the above command, SVN ID is 1.
The above command calls into the APIs provided by the Manifest generation tool and the signer tool. It is equivalent to running these commands:
1. Generate public key from OS_priv.pem.
2. Create the OS Manifest hash file.
3. Sign the OS Manifest hash file.
4. Generate the OS Manifest.

## Slide 20
Steps to sign an OS Manifest
Strip the OSIP header from boot.bin -> no_osip_boot.bin
dd if=boot.bin of=no_osip_boot.bin bs=512 skip=1 conv=notrunc
Run ISU with no_osip_boot.bin. ISU will generate the OS Manifest.
./isu -i no_osip_boot.bin -o manifest_name -l OS_priv.pem -v 1 -t 6 -p 2
Attach the OS Manifest to no_osip_boot.bin.
dd if=manifest_name_OS_manifest.bin of=secure_boot.bin bs=1024 count=1 conv=notrunc
dd if=no_osip_boot.bin of=secure_boot.bin bs=1024 seek=1 conv=notrunc
Run secure_boot.bin through xfstk stitcher to generate a complete boot.bin.
xfstk-stitcher -k baytrail_OS.xml -c baytrail_OS_config.txt
(See slide 18 for location of files)
Zip the boot.bin in the OS image.
Flash OS image onto the platform.
Note: An INT IFWI (unsigned) is required to be able to flash a signed OS image. So the sequence is:
Flash an INT IFWI (unsigned IFWI)
Flash Signed OS
Flash EXT IFWI (signed IFWI)

## Slide 21
Paths for tools and other files
Keys
umg/security/byt-security/PSI_TOOLS/keys
OS keys are also checked in at
  a/bsp/vendor/intel/PRIVATE/cert
ISU
a/bsp/device/intel/PRIVATE/intel_signing_utility/isu
Or
umg/tools/isu/bin/linux/openssl/isu
OS Stitching
Download xfstk-stitcher from xfstk.intel.com
Xml and config file at
  umg/tools/stitchOS
FITC
Baytrail FITc v.1.0.0.1050v2 (http://xfstk.intel.com/baytrail.htm )
Notes: <number>